## Slide 1: Spring Leaf-Off Imagery for Minnesota
July 1, 2010

## Slide 2: Agenda for Today’s Meeting
Introductions and Overview
Project Specifications
Acquisition Regions
Control Targets
Partnership Opportunities & Schedule

## Slide 3: Steering Committee
Steve Kloiber – MnDNR
  Primary funding partner; technical guidance
Chris Cialek – MnGeo
  Project management, coordination, contracting
Pete Jenkins – MnDOT
  Control target coordination; technical guidance

## Slide 4: Overview
Statewide project to collect leaf-off color imagery over 5 years
Spurred on by DNR efforts to update wetlands mapping
0.5-meter (20-inch) nominal resolution
Offer local partnership options to buy-up at improved 1-foot res.

## Slide 5: Project Specifications Four Spectral Bands
Natural Color
Color Infrared
Blue
Green
Red
Near IR

## Slide 6: Project Specifications – Leaf-Off

## Slide 7: Project Specifications – Leaf-Off
Seasonally High Water Table
Better view of the land beneath the tree canopy

## Slide 8: Project Specifications - Format
Digital ortho-rectified quarter quad
  *.tif
Compressed county mosaic
  *.jp2
Digital stereo pairs

## Slide 9: Project Specifications - Resolution
50-cm or 30cm

## Slide 10: Why Not Six-Inch Resolution?
Tight time window
Large, complex project
Managing risk
  Reduce the number of variables
  Reduces flying time (limit the scope)
Cost vs. benefit consideration

## Slide 11: Resolution Comparison
1 inch = 200 feet (1:2400)
1 inch = 100 feet (1:1200)
1 inch = 50 feet (1:600)

## Slide 12: Project Specifications – Positional Accuracy
Map Scale | Ground Sample Resolution | NMAS RMSE-c (ft) | NMAS Accuracy 95% (NSSDA) (ft) | ASPRS RMSE-c (ft) | ASPRS Accuracy 95% (NSSDA) (ft)
1:3,000 | 0.30 m / 0.98 ft | 5.49 | 9.50 | 3.54 | 6.12
1:5,000 | 0.50 m / 1.64 ft | 9.15 | 15.8 | 5.80 | 10. 0
1:10,000 | 1.00 m / 3.28 ft | 18.3 | 31.6 | 11.6 | 20.1
Tested 95% Accuracy
Northeast 2009 = ±11.5 ft

## Slide 13: Northeast Acquisition - 2009
Funding Partners
  DNR / ENTRF
  MPCA
  St. Louis County
  USGS/NGA
10.5 Million Acres

## Slide 14: East-Central Acquisition - 2010
Funding Partners
  DNR / ENTRF
  Metropolitan Council
  USGS/NGA
  Scott County
  Dakota County
  MMCD
In-Kind Partners
  MnGeo
  MnDOT
4.5 Million Acres

## Slide 15: South Acquisition - 2011
Funding Partners
  DNR / ENTRF
  ??
In-Kind Partners
  MnGeo
  MnDOT
  ??
4.5 Million Acres
15.3 Million Acres

## Slide 16: 2008 FSA Target Inventory

## Slide 17: 2011 Target Requirements
Two ways to capture target data
Targets (2008)
Physical features

## Slide 18: Single Leg Template

## Slide 19: Completed Target

## Slide 20: Physical Features

## Slide 21: Documentation
2008 FSA Observation Sheet
Use the same form
Pictures are necessary
Will share data with FSA

## Slide 22: What is Needed?
Existing targets need to be re-painted
New targets for counties with low numbers
Follow up with documentation

## Slide 23: Partnership Opportunities
0.5-meter data provided at no cost
Option to buy-up to 1-foot
  Cost estimate (based on previous recent experience) ~ $24/square mile
Assist in target placement or refreshing

## Slide 24: Acquisition Schedule
November 2010
  Partner agreements drafted
  RFP released
December 2010
  Vendor selection
  Finalized partner agreements
January 2011
  Finalize contract
March 2011
  Set / refresh targets
April/May 2011
  Acquire imagery
September 2011
  Data delivery
October 2011
  Final QA/QC review

## Slide 25: Spring Leaf-Off Imagery for Minnesota
THANK YOU FOR ATTENDING
Q & A
steve.kloiber@state.mn.us
651.259.5164
chris.cialek@state.mn.us
651.201.2481
peter.jenkins@state.mn.us
651.366.3457